## Slide 1: Network layer in aws
VPC. Subnet. Route table. NAT and Internet gateway. Security group. NACL.

## Slide 2: Preface – TCP/ip model
OS
Driver
MAC address

## Slide 3: Preface – TCP/ip model
Route table
Route table
Border Gateway Protocol

## Slide 4: ip addresses
Internet Protocol v4 address is 32bit number (IPv6 128 bit)
Address space is 232 = 4,294,967,296 IPs
IP Notation: 0.0.0.0 to 255.255.255.255
Subnet mask – number of bits dedicated for network address (subnet)
CIDR Notation: /0 to /32
Remaining part is for host address
Example of CIDR Block: 10.0.0.0/24

## Slide 5: NETWORKs and HOSTS
Network (24bits) Hosts (8bits)
CIDR block: 10.0.0.0/24 = 00001010.00000000.00000000.00000000
Mask: /24 = 255.255.255.0 = 11111111.11111111.11111111.00000000
Hosts: 232-24=28=256 ={00001010.00000000.00000000.00000000 -
00001010.00000000.00000000.11111111}=
={10.0.0.0 - 10.0.0.255}
Hosts in 10.0.0.0/24 are from 10.0.0.0 to 10.0.0.255

## Slide 6: Subnetting and CIDR
The practice of dividing a network into sub-networks
Example:
Network 10.0.0.0/24 10.0.0.0 – 10.0.0.255
Subnet 1 10.0.0.0/25 10.0.0.0 – 10.0.0.127
Subnet 2 10.0.0.128/25 10.0.0.128 – 10.0.0.255
Classless Inter-Domain Routing (CIDR)
  Fixes issues with previous Classful addressing
  Variable-length subnet masking
Notes: Clasful

## Slide 7: NETWORKs and HOSTS SUBNET1
Network (26bits) Hosts (6bits)
CIDR block: 10.0.0.0/26 = 00001010.00000000.00000000.00000000
Mask: /26 = 255.255.255.192 = 11111111.11111111.11111111.11000000
Hosts: 232-26=26=64 ={00001010.00000000.00000000.00000000 -
00001010.00000000.00000000.00111111}=
={10.0.0.0 - 10.0.0.63}
Hosts in 10.0.0.0/26 are from 10.0.0.0 to 10.0.0.63

## Slide 8: NETWORKs and HOSTS SUBNET2
Network (26bits) Hosts (6bits)
CIDR block: 10.0.0.64/26 = 00001010.00000000.00000000.01000000
Mask: /26 = 255.255.255.192 = 11111111.11111111.11111111.11000000
Hosts: 232-26=26=64 ={00001010.00000000.00000000.01000000 -
00001010.00000000.00000000.01111111}=
={10.0.0.64 - 10.0.0.127}
Hosts in 10.0.0.0/26 are from 10.0.0.64 to 10.0.0.127

## Slide 9: NETWORKs and HOSTS SUBNET3
Network (26bits) Hosts (6bits)
CIDR block: 10.0.0.128/26 = 00001010.00000000.00000000.10000000
Mask: /26 = 255.255.255.192 = 11111111.11111111.11111111.11000000
Hosts: 232-26=26=64 ={00001010.00000000.00000000.10000000 -
00001010.00000000.00000000.10111111}=
={10.0.0.128 - 10.0.0.191}
Hosts in 10.0.0.0/26 are from 10.0.0.128 to 10.0.0.192

## Slide 10: NETWORKs and HOSTS SUBNET4
Network (26bits) Hosts (6bits)
CIDR block: 10.0.0.192/26 = 00001010.00000000.00000000.11000000
Mask: /26 = 255.255.255.192 = 11111111.11111111.11111111.11000000
Hosts: 232-26=26=64 ={00001010.00000000.00000000.11000000 -
00001010.00000000.00000000.11111111}=
={10.0.0.192 - 10.0.0.255}
Hosts in 10.0.0.0/26 are from 10.0.0.192 to 10.0.0. 255

## Slide 11: Private networks
Originated from IPv4 address exhaustion but now used for security
IP addresses reserved for Private networks
  10.0.0.0/8 , 172.16.0.0/12 or 192.168.0.0/16
Private IP packets not routed in Internet
Network address translation (NAT) between Private networks and Internet (or other Private networks)
  Mapping between IP addresses from different address spaces

## Slide 12: Q&A

## Slide 13: AWS VPC
What is VPC?
Deployment
CIDR blocks
Single,Multi-VPC and Multi-account setup
Accounts and VPC management

## Slide 14: What is VPC?
Amazon Virtual Private Cloud
A virtual network residing in you AWS account
Supports IPv4 & IPv6
Defined by CIDR block
Notes: The architectural need - You need to deploy and manage AWS resources in a networked environment that provides workload isolation.
Your private network space in the AWS Cloud
Provides logical isolation for your workloads: Dev,Test
Allows custom access controls and security settings for your resources
IPv4 vs. IPv6
Classless Inter-Domain

## Slide 15: VPC Deployment
Located in 1 of 22 AWS Regions
Can host resources in any
Availability Zone within its Region

## Slide 16: CIDR block of vpc
Each VPC reserves a range of private IP addresses
These addresses are available for use by resources deployed in that VPC
Defined using CIDR
Example: 10.0.0.0/16 = all 65,536 IPs from 10.0.0.0 to 10.0.255.255

## Slide 17: Single-VPC
Very limited use cases like :
Single application
High-performance computing
Cons:
No isolation of internal and external threats
Complex to maintain Privileges
Pros:
No accounts to maintain
Easy to see all resources
Notes: Does not provide isolation
Easier to maintain than multiple accounts

## Slide 18: Multi-VPC
Pros:
Network level / External threats isolation
Cons:
Complex to maintain Least Privileges
Internal risks
Notes: VPC1 = App1-Dev
VPC2 = App1-Prod
VPC3 = App2-Dev
VPC4 = App2-Prod

## Slide 19: Mutli-account
Use case:
Multiple applications and environments
Big organizations
Pros
Best isolation
DIAGRAM
Cons
Harder to maintain
Notes: Account per Application and Environment

## Slide 20: Accounts management
AWS Control Tower
AWS Organizations
AWS SSO
AWS Config
DIAGRAM
Notes: Account per Application and Environment

## Slide 21: VPC limits
5 VPCs per region per account
5 Elastic IP addresses per Region
200 subnets per VPC
Soft limits vs hard limits
Example:
IPv4 CIDR blocks per VPC - Default: 5 Max: 50
IPv6 CIDR blocks per VPC - Default: 1 Max: 1
More:
https://docs.aws.amazon.com/vpc/latest/userguide/amazon-vpc-limits.html
Notes: Some limits for example
They have sensible values.
Some are hard to reach.
Some can be increased.

## Slide 22: RELATED AWS SERVICES
Manage network routing & security
Subnets
Route tables
Security groups
Network ACLs
Internet Gateway
NAT Gateway
Endpoints
VPNs
Peering Connection
Transit Gateway
Traffic mirroring

## Slide 23: Q&A

## Slide 24: DEMO
AWS VPC Demo

## Slide 25: SUBNETS
Key Attributes, Public & Private subnet. Internet Gateway. NAT Gateway.

## Slide 26: SUBNETS – Key attributes
Subset of VPC CIDR Block
Subnets cannot overlap
Reside in only one AZ
5 IPs from each Subnet are reserved for Amazon

## Slide 27: Subnets - example
VPC CIDR Block 10.0.0.0/24 = 256 hosts
divided in 4 subnets, 64 host per subnet (59 available)
2 public and 2 private subnets
in 2 Availability Zones

## Slide 28: Subnets - public and private
Public subnets:
Reachable from the internet (inbound traffic) through Internet Gateway
Contains Private IPs
Private subnets:
Not directly reachable from the Internet
Allow access to the internet (outbound traffic) through NAT Gateway
Not AWS resource types. They are configuration and a standard practice.

## Slide 29: Subnets - public and private

## Slide 30: Subnets – Usage examples
Databases  Private subnet
Back-end  Private subnet
  Private API
  Batch/Scheduled processing
  External Applications Integration
HTTP server/Public API  Public subnet

## Slide 31: Route tables
Direct network traffic
Contains row for each routing rule
Precedence of more specific destination
Each VPC has a default route table
Best to have one route table for each subnet
Public Subnet - Route Table: Private Subnet - Route Table:
All traffic is directed to Internet Gateway All traffic directed to NAT Gateway
Notes: Subnets which have no explicit associatin with Route Table are associated with the default RT

## Slide 32: Internet gateway
Allows communication with Internet
Acts as NAT between public and private IPs
Horizontally scaled, redundant, highly-available

## Slide 33: NAT gateway
Allows outbound traffic from the private subnet to the Internet
Prevents inbound traffic from the Internet to the private subnet
Has Elastic IP

## Slide 34: Routing example
Notes: Inbound Public
Outbound public
Outbound Private
Inbound Private

## Slide 35: Q&A

## Slide 36: DEMO
AWS VPC Demo

## Slide 37: Lab time
Time for you to practice
Lab Exercise - Part I to IV

## Slide 38: Security
Security groups. NCLs.

## Slide 39: Security groups
Virtual Firewalls
Restrict by Protocol TCP/UDP, Port, IP
Only Allow rules
Stateful (remembers if traffic is a response to a request in the opposite direction)
Attached to AWS resources explicitly
Provides fine granularity and flexibility
Default - Outbound: All, Inbound: None

## Slide 40: Network ACLs
Firewalls
Restrict by Protocol TCP/UDP, Port, IP
Both Allow and Deny
Stateless (does not remember where the traffic is initiated)
Attached at subnet boundary and implicitly applied to all instances
Provides prevention from too bread access
Default – Outbound: Allow All, Inbound: Allow All

## Slide 41: vpc example

## Slide 42: Real life example

## Slide 43: Q&A

## Slide 44: DEMO
AWS VPC Demo

## Slide 45: Other services
Endpoints and Endpoint Service
  Enables access to AWS Services without leaving the Amazon network
  Does not require internet gateway, NAT, VPN or AWS Direct Connect
VPNs
  Site-to-Site IP Sec VPN (Layer 3 OSI)
  Virtual Private Gateway
    AWS side
  Customer Gateway
    Client side
Peering Connections
Transit Gateway
  Connect VPCs, AWS Direct Connect, and AWS Site-to-Site VPN connections
  Examples: https://docs.aws.amazon.com/vpc/latest/tgw/transit-gateway-centralized-router.html
Traffic Mirroring
  Direct copy of all traffic to external appliance for security and monitoring

## Slide 46: Lab time
Time for you to practice
Lab Exercise - Part V and VI